## استخدام المبيد الحشرى ساتيرن كمثبط لتآكل الحديد المجلفن فى مياه الصرف الصحى وتأثيره البيولوجي على بكتريا القولون.

محمود سلامة محمود الهايشة

mahmoud_elhaisha@yahoo.com

2019 / 8 / 26

Satirn as pesticide inhibitor for the corrosion of the galvanized iron in wastewater and its biological effect on Escherichia coli.

Satirn is a type of the pesticides has been evaluated as green inhibitor for the corrosion of the galvanized iron in saline solution which was investigated by chemical and electrochemical measurements. The results of polarization showed that satirn acts as mixed type inhibitor. Inhibition was found to increase with the increase of satirn concentration reaching to approximately 90% at 250 ppm. The inhibitive action was discussed by the adsorption of a stable complex on the metal surface. The adsorption of satirn on the metal surface obeys Temkin adsorption isotherm. Satirn has a slightly effect on Escherichia coli and can be applied safely in sanitation plants.

استخدام المبيد الحشرى ساتيرن كمثبط لتآكل الحديد المجلفن فى مياه الصرف الصحى وتأثيره البيولوجي على بكتريا القولون.

تم دراسة تأثير المبيد الحشرى ساتيرن كمثبط صديق للبيئة لتآكل الحديد المجلفن في الماء المالح باستخدام تقنيات فقدان الوزن وإستقطاب الجهد الديناميكى والمقاومة الكهروكيميائية الطيفية (EIS) والكهروكيميائية متغيرة التردد (EFM) وأظهرت النتائج أن الساتيرن في الماء المالح هو مانع جيد للتآكل مع كفاءة تثبيط وصلت إلى 90% في 250 جزء في المليون من المبيد من خلال تشكيل طبقة ممتزة على سطح المعدن تحميه من تآكل البيئة المؤكسدة. إمتزاز الساتيرن على سطح الصلب طبيعياً ويتبع نظرية تمكن Temkin للإمتزاز الأيسوثرم ويعمل كمثبط مختلط. وتظهر الدراسة لهذا المبيد تأثير طفيف على النشاط الحيوى لبكتريا القولون وعلى ذلك يمكن تطبيقه بأمان في محطات معالجة مياه الصرف الصحى.

Ref:

Add El-Aziy S. Fouda, Ayman Y. El-Khateeb, Mohamed Fakih and Aly M. El-azaly (2015). Satirn as pesticide inhibitor for the corrosion of the galvanized iron in wastewater and its biological effect on Escherichia coli. Zaštita Materijala, 56(1), 81-91. https://doi.org/10.5937/zasmat1501081f

(نشر بتصرف)

https://www.ahewar.org/

الحوار المتمدن