## دراسة مقارنة الوسائط الصلبة المختلفة فى الأراضي الأفقية الرطبة ومعدلات التدفق

محمود سلامة محمود الهايشة

mahmoud_elhaisha@yahoo.com

2019 / 7 / 30

Comparative Study On Different Horizontal Subsurface Substrates In Flow Wetlands.

All experiments were carried out on a field-scale, subsurface, subsurface wetland system at the Sherbeen Wastewater Treatment Plant in Sherbeen City, Sherbeen, Dakahlia Governorate, Egypt. A greenhouse experiment has been conducted to study the effect of using different wetland substrates that have been compiled on the basis of effluent treatment efficiency. Wetland beds have been prepared with locally available plants, in particular (Phragmites Australis). The effectiveness of the treatment was evaluated on parameters such as biological oxygen demand (BOD), chemical oxygen demand (COD), total Kjeldahl nitrogen (TKN), total suspended solids (TSS) and total phosphorus (TP). The results indicate that nutrient reduction corresponds to lower flow in wetland beds. At the lower flow rate of 2.34 m3/day, the system with plastic supports showed the highest removal efficiencies of BOD, COD, TKN, TSS and TP in percentages of 74.42, 74.9 %, 63.28, 87.49 and 71.29 %, correspondingly.

دراسة مقارنة الوسائط الصلبة المختلفة فى الأراضي الأفقية الرطبة ومعدلات التدفق.

في هذا البحث تم اجراء تجربة لدراسة تأثير استخدام وسائط مختلفة في أحد محطات الأراضي الرطبة المشيدة بمركز شربين بمحافظة الدقهلية على كفاءة الإزالة للعناصر المختلفة في مياه الصرف الصحي تم تجهيز خلايا الأراضي الرطبة وزرعها بأحد النباتات المحلية )البوص) ، حيث تم تقييم كفاءة إزالة العناصر مثل الأكسجين البيولوجي الممتص BOD والأكسجين الكيميائي الممتص COD والنيتروجين الكلى TKN والمواد الصلبة الكلية العالقة TSS والفوسفات الكلى TP وقد اوضحت النتائج انخفاض في نسبة العناصر السابقة في المياه الخارجة وذلك عند اقل معدل تدفق للمياه الداخلة الى خلايا الأراضي الرطبة حيث انه عند معدل تدفق 2.34 م 3 /يوم . أظهرت النتائج أن الخلية المستخدم بها البلاستيك كوسط ذات أعلى كفاءة في إزالة عناصر الأكسجين البيولوجي الممتص BOD والأكسجين الكيميائي الممتص COD والنيتروجين الكلى TKN المواد الصلبة الكلية العالقة TSS والفوسفات الكلى TP بالنسب التالية 74.42 و 74.90 و 63.28 و 87.49 و 71.29 % على الترتيب .

Ayman Y. El-Khateeb, M. H. Mahmoud, M. Fakih (2019). Comparative study on different horizontal subsurface substrates in flow wetlands. Progress in Chemical and Biochemical Research, 2(1), 20-23. https://doi.org/10.33945/sami/pcbr.2019.2.2023

(نشر بتصرف)

https://www.ahewar.org/

الحوار المتمدن